## Slide 1
Results Summary: Fixed → PMMH → Reference Library
Dataset | Configuration | RMSE (cyc.) | MAPE | Coverage
FD001 | Fixed parameters | 98.3 | 1.35 | 0.49
FD001 | PMMH | 52.9 | 0.77 | 0.68
FD001 | Library, one-shot | 44.3 | 0.63 | 0.75
FD003 | Fixed parameters | 160.4 | 2.45 | 1.00
FD003 | PMMH | 104.6 | 1.72 | 1.00
FD003 | Library, one-shot | 100.1 | 1.54 | 0.99
Nominal target coverage is 0.90. FD001 rises monotonically toward it (0.49 → 0.68 → 0.75); FD003 is over-conservative from the start (already 1.00 under fixed parameters).
RMSE roughly halves at each stage on both datasets — the library is the best point-accuracy AND best-calibrated configuration reached.
One-shot library beats periodic re-matching on both fleets (FD001: 44.3 vs 47.3; FD003: 100.1 vs 107.5) — tested, not assumed.
1

## Slide 2
The Three Model Configurations, Side by Side
Configuration | Degradation rate k | Process noise σᵥ | How it was obtained
Fixed parameters | Pooled regression — one rate for the whole fleet (FD001 ≈ 0.0028) | 0.5 — hand-set, not estimated | k: log-linear regression on pooled (cycle, Health Index) data, all training engines together. σᵥ: an arbitrary starting value, never fitted.
PMMH | Per engine (mean ≈ 0.0039 FD001 / ≈ 0.0018 FD003); non-converged engines fall back to the pooled rate above | ≈ 0.66 — fleet-wide, pooled from converged per-engine posteriors | Particle Marginal Metropolis-Hastings: samples the joint posterior p(k, σᵥ ¦ data) using the bootstrap filter's own likelihood. Converged on 31/100 (FD001), 8/100 (FD003) engines.
Reference library (one-shot) | Per engine, matched from a library of 100 individually-fitted engine rates (library mean k ≈ 0.0037, FD001) | ≈ 0.66 — same fleet-wide value as PMMH, not re-estimated | Test engine's observed Health Index (after a 20-cycle warm-up) matched via Maximum Mean Discrepancy to its 5 nearest library engines, rates averaged. Matched once, held fixed after — one-shot beat periodic re-matching empirically.
σw (measurement noise, ≈ 9.26) is fitted once from training-residual spread and reused unchanged across all three — it is not a point of difference between them.
The state-space model itself — exponential dynamics, Gaussian noise family, observation model, initial distribution — is identical in all three configurations. Only how k and σᵥ are obtained changes.
2

## Slide 3
Why Not a Kalman Filter?
 | Kalman Filter | Particle Filter (used here)
State transition | Exact closed-form update needs linear dynamics + Gaussian noise | Handles any transition — here it's affine anyway, so this alone wouldn't rule out a KF
Transition noise family | Locked to Gaussian — a skew-normal noise (tested, mild AIC gain) breaks the closed-form recursion | No closed form needed — the bootstrap filter just samples the noise; any density works unchanged
RUL is the real target | Gives one Gaussian belief over the state — not a threshold-crossing time, and no natural way to handle a threshold that is itself random | Keep simulating each particle forward and record when it crosses its own (randomly drawn) failure level — a first-passage time, for free
Parameter estimation (PMMH) | Only has an exact closed-form likelihood while the model stays Gaussian; a different noise family means re-deriving it | Already produces an unbiased likelihood estimate as a byproduct of ordinary filtering — reused as-is by PMMH, whatever the noise family
The health-index transition itself, x_t = 100 − (100 − x_{t-1})·eᵏ + v_t, is actually affine in x_{t-1} — nothing there alone rules out a Kalman filter.
What does: RUL is a first-passage time against a per-particle random failure threshold, and the noise family was deliberately left open — both need a simulation-based posterior, not a single Gaussian summary.
3

## Slide 4
Health Tracking & Particle Diversity
Pooled Health-Index RMSE, all 13,096 FD001 test cycles: 0.082 (PMMH) vs. 0.092 (fixed parameters) — filtered estimate stays within about a tenth of a unit of the observed Health Index throughout.
Effective sample size stays healthy: mean ESSₜ / N = 0.79 (SD 0.02), fleet-wide — the particle cloud is never close to degenerate.
Adaptive resampling triggers at τ = 0.5: at least half the particles (250 / 500) always support the posterior.
Systematic weakness: trajectory RMSE correlates with observation length (r = −0.58) — shortest-observed quartile averages 111 cycles RMSE vs. 61 for the longest. This is a degradation-rate estimation limitation, not a filter/tracking failure — the filter tracks even the worst-observed engine's health well; the error shows up later, downstream, in the RUL projection.
4

## Slide 5
Parameter Estimation via PMMH
Dataset | σᵥ (est.) | σᵥ (hand-set) | k (growth rate) | Chains converged
FD001 | ≈ 0.66 | 0.5 | ≈ 0.0039 | 31 / 100
FD003 | ≈ 0.66 | 0.5 | ≈ 0.0018 | 8 / 100
PMMH jointly estimates (k, σᵥ) per engine — N = 3200 particles, 1000 iterations, acceptance-rate convergence rule ≥ 0.10.
Non-converged chains fall back to the pooled regression-fitted rate — every engine still contributes an estimate, none are dropped.
The fitted σᵥ ≈ 0.66 confirms the hand-set default (0.5) understated the true process noise, on both datasets.
Convergence is a named limitation, not hidden: a single global random-walk step size mixes unevenly across a diverse fleet, worse on FD003's noisier two-fault-mode likelihood surface.
5

## Slide 6
Censoring & Failure-Threshold Calibration
Dataset | Fleet-mean censored | Median engine | Engines > 10%
FD001 | 5.3% | 0.2% | 16 / 100
FD003 | 29.7% | 31.1% | 80 / 100
Censoring: a particle that hasn't crossed the failure threshold by r_max is recorded as RUL = r_max, piling mass at the cap — biases the reported posterior slightly narrow and to the left. Reported coverage includes this effect as-is, not corrected out.
The single biggest jump in calibration (coverage 0.000 → 0.49) came entirely from calibrating the failure threshold in posterior space — not from PMMH or the library. Degradation parameters were identical between those two configurations.
Subsequent jumps are attributed separately: 0.49 → 0.68 (PMMH, data-driven σᵥ/k) → 0.75 (library, per-engine matched rate).
6

## Slide 7
The Central Trade-Off: Accuracy vs. Calibrated Uncertainty
Dataset | Model | RMSE (cyc.) | MAPE | Coverage
FD001 | Linear regression baseline | 32.0 | 0.53 | —
FD001 | Library, one-shot (this thesis) | 44.3 | 0.63 | 0.75
FD003 | Linear regression baseline | 58.2 | 1.07 | —
FD003 | Library, one-shot (this thesis) | 100.1 | 1.54 | 0.99
The baseline is the sharper point predictor on both datasets — reported plainly, not downplayed.
But the baseline produces one number with no expression of confidence — "does its 90% interval cover the truth?" is not a question that can even be posed of it.
The particle filter concedes point accuracy in exchange for a calibrated credible interval a bare point estimate cannot structurally provide. For a maintenance decision, that is the quantity that matters.
7

## Slide 8
Limitations & Future Work
σᵥ is still fleet-wide, not per-engine — PMMH estimates it per engine, but converged posteriors are pooled into one number applied to every test engine. The growth rate k is the only parameter with genuine per-engine treatment (via the library). Top future-work priority: better PMMH convergence + a genuinely per-engine σᵥ — it addresses FD001's overconfidence and FD003's over-conservatism at once.
Similarity matching simplifies Cai et al. (2020) in three ways: a scalar Health Index instead of the full sensor feature matrix; top-5-nearest instead of a formal statistical accept/reject test; a matched rate held fixed between matches rather than tracked jointly with the state online.
No operating-condition-aware normalisation — the pipeline does not extend to FD002 / FD004 (multiple operating conditions) as-is. A scoped, well-defined next step, not an open research question.
8

## Slide 9
Acknowledgements
My sincere thanks to my promotor, Prof. Dr. Koen De Turck, and my co-promotor, Prof. Dr. Dieter Fiems, for their guidance, patience, and careful reading throughout this thesis.
And to my wife, Shamim Sattarpour Nobari, who lived every part of this journey with me — this work is as much hers as it is mine.
Thank you for your attention.
9