## Slide 1
A BAYESIAN APPROACH TO DIGITAL TWINS
Sequential Monte Carlo for Turbofan Engine Remaining Useful Life Estimation
Sajjad Ayashm
Master of Science in Statistical Data Analysis · Ghent University
Promotor: Prof. Dr. Koen De Turck · Co-promotor: Prof. Dr. Dieter Fiems
Academic Year 2025 – 2026
Notes: Good morning / afternoon. My name is Sajjad Ayashm, and today I will present my master's thesis: a Bayesian approach to digital twins, applying Sequential Monte Carlo -- a particle filter -- to estimate the remaining useful life of turbofan engines. My promotor was Prof. De Turck, co-promotor Prof. Fiems.

## Slide 2
MOTIVATION
A Single Number Is Not Enough
Predictive maintenance schedules repairs from an asset's actual condition, not a fixed calendar. The key quantity: Remaining Useful Life (RUL) — cycles left before failure. Most methods — regression, CNN, LSTM — output one number and nothing else.
A point-estimate model gives you:
RUL ≈ 50 cycles
But which is it, really?
POSSIBLE TRUTH A
50 ± 3
Confident.
Safe to schedule service at cycle 45.
POSSIBLE TRUTH B
50 ± 40
Uncertain.
Could fail anywhere from cycle 10 to 90.
A point estimate can't tell you which one you're actually in.
2
Notes: Predictive maintenance means: use sensor data to decide when to service a machine, instead of a fixed schedule or waiting for it to break. The number everyone wants is the Remaining Useful Life -- how many cycles are left. But almost all published methods, from simple regression to deep neural networks, give you just one bare number, like fifty cycles -- no range attached at all. Here is why that is a problem: behind that same fifty, the truth could look like 'fifty, plus or minus three' -- confident, safe to schedule service soon -- or it could look like 'fifty, plus or minus forty' -- so uncertain the engine could fail anywhere from cycle ten to ninety. These call for completely different maintenance decisions. But a bare point estimate cannot tell you which of these two worlds you're actually in, because it was never built to describe uncertainty in the first place. That is the gap this thesis is about.

## Slide 3
RESEARCH OBJECTIVE
A Probabilistic Digital Twin
Build a per-engine particle filter that:
1
Tracks the posterior distribution of engine health from noisy sensors
2
Extracts a full RUL distribution — a median with a 90% credible interval
3
Is evaluated on whether that interval is calibrated — not just accurate
Evaluated on NASA C-MAPSS (FD001, FD003) — full 100-engine test fleets, not a sample.
Sensors
(21 channels)
Health Index
(1 scalar)
Particle
Filter
RUL
Distribution
Updated every cycle, as new sensor data arrives
3
Notes: So the objective of this thesis is precise: build, implement, and validate a particle filter that does two things -- track the posterior of an engine's health from noisy sensors, and turn that posterior into a full RUL distribution, a median plus a 90 percent credible interval. And then -- this is the important part -- actually test whether that interval is calibrated: does the 90 percent interval really contain the true remaining life about 90 percent of the time? Not assume it, test it. Everything is evaluated on the NASA C-MAPSS benchmark, on the full one-hundred-engine test fleets of two sub-datasets, FD001 and FD003, not a cherry-picked sample.

## Slide 4
METHOD CHOICE
Why Not a Simpler Filter (Kalman)?
A Kalman filter is exact when the model is linear-Gaussian and unconstrained. None of that fully holds here:
1
Bounded, one-sided state
Health lives in [0,100] and only degrades. A Gaussian posterior spreads over the whole real line — it can't respect that.
2
Flexible noise
Measurement noise fits a skew-normal slightly better than Gaussian. A particle filter doesn't require Gaussianity at all.
3
RUL is a first-passage time
The time to cross a failure threshold is non-Gaussian by nature — it needs Monte-Carlo simulation anyway, which particles already provide.
4
Notes: Why not just use a Kalman filter, which is simpler? A Kalman filter is the exact, closed-form answer when three things hold: the model is linear, the noise is Gaussian, and the state is unconstrained. Three things push us away from that here. First, health is bounded between 0 and 100 and should mostly go one way -- a Gaussian doesn't respect boundaries. Second, our measurement noise fits a little better as a skew-normal than a Gaussian, and a particle filter does not force us to choose Gaussian. Third, and most important: what we actually want, the Remaining Useful Life, is a first-passage time -- the cycle where health first crosses a threshold. That is non-Gaussian even if the health posterior itself were Gaussian, so we need Monte Carlo simulation at that stage regardless. A particle filter gives us that machinery for free.

## Slide 5
THE MODEL — PART 1
One Number to Summarize Engine Health
21 raw sensors → 10 selected (drop constant / redundant channels) → combined into a single Health Index h ∈ [0,1] (weighted average, min–max normalised, oriented to decrease with wear) Degradation dynamics: exponential decay —
matches the shape the C-MAPSS simulator itself uses.
Chart: Illustrative Health-Index trajectory
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29
Health Index (posterior median) | 100 | 95.1229 | 90.4837 | 86.0708 | 81.8731 | 77.8801 | 74.0818 | 70.4688 | 67.032 | 63.7628 | 60.6531 | 57.695 | 54.8812 | 52.2046 | 49.6585 | 47.2367 | 44.9329 | 42.7415 | 40.657 | 38.6741 | 36.7879 | 34.9938 | 33.2871 | 31.6637 | 30.1194 | 28.6505 | 27.2532 | 25.924 | 24.6597 | 23.457
+1 band | 100 | 100 | 96.4837 | 92.0708 | 87.8731 | 83.8801 | 80.0818 | 76.4688 | 73.032 | 69.7628 | 66.6531 | 63.695 | 60.8812 | 58.2046 | 55.6585 | 53.2367 | 50.9329 | 48.7415 | 46.657 | 44.6741 | 42.7879 | 40.9938 | 39.2871 | 37.6637 | 36.1194 | 34.6505 | 33.2532 | 31.924 | 30.6597 | 29.457
-1 band | 94 | 89.1229 | 84.4837 | 80.0708 | 75.8731 | 71.8801 | 68.0818 | 64.4688 | 61.032 | 57.7628 | 54.6531 | 51.695 | 48.8812 | 46.2046 | 43.6585 | 41.2367 | 38.9329 | 36.7415 | 34.657 | 32.6741 | 30.7879 | 28.9938 | 27.2871 | 25.6637 | 24.1194 | 22.6505 | 21.2532 | 19.924 | 18.6597 | 17.457
Same construction is fit on FD001 only, then reused unchanged on FD003 as a robustness check.
5
Notes: Now, what does the digital twin actually track? We start from twenty-one raw sensor channels, drop the ones that are constant or redundant, and keep ten. These ten are combined into one single number, the Health Index, between 0 and 1, where 1 is healthy and 0 is failed. Over time, this Health Index is modelled as decaying exponentially. That is not an arbitrary choice: NASA's own C-MAPSS simulator, which generated this data, documents that its underlying damage process is exponential. Importantly, this whole construction -- which sensors, which weights, which shape -- is fit only on the FD001 dataset, and then reused without any changes on FD003, so FD003 becomes a genuine robustness test rather than a re-tuned model.

## Slide 6
THE MODEL — PART 2
The Bootstrap Particle Filter Loop
1. Predict
Every particle moves forward one cycle through the degradation model, each drawing its own noise.
2. Weight
Each particle is scored by how well it matches the new sensor reading — Health Index likelihood.
3. Resample
When the Effective Sample Size drops below 50% of N, low-weight particles are dropped and duplicated.
→ repeated every cycle, independently, for each of the 100 engines
N = 500 particles per engine. Systematic resampling (low variance). Fleet-wide effective sample size stays at 79% of N on average — the particle cloud never collapses.
6
Notes: Mechanically, the particle filter is a simple three-step loop, repeated every cycle for every engine independently. Predict: each of five hundred particles steps forward through the degradation model, each with its own random noise. Weight: each particle gets a score for how well it matches the newest sensor reading. Resample: when a diagnostic called the Effective Sample Size falls below half of N, we drop the low-weight particles and duplicate the good ones, so we don't waste computation on particles nobody believes in anymore. Across the entire hundred-engine fleet, this effective sample size averages seventy-nine percent of N -- meaning the particle cloud stays healthy and diverse, it never collapses onto one or two particles.

## Slide 7
THE MODEL — PART 3
From Posterior to a RUL Distribution
Forward-simulate the whole particle cloud until each particle crosses a failure threshold → one RUL sample per particle → a full distribution, not one value. Problem found: real engines fail around health ≈ 0.26 (observed) — but the filter's own posterior runs higher, ≈ 0.34, at that same moment. Fix: calibrate the failure threshold in the filter's own posterior space, and draw it per-particle from a distribution — not one fixed number.
90% credible-interval coverage
0.000 → 0.75 / 0.99
This single fix was the largest jump in the whole thesis — from a categorical failure to a usable interval.
7
Notes: Here is the single most important fix in the thesis. Once the filter has a posterior over health, we simulate every particle forward until it crosses a failure threshold -- that crossing cycle is one sample of RUL, and collecting one sample per particle gives a full RUL distribution, not just one number. But early on, this distribution was badly wrong: the ninety percent credible interval covered zero out of the test engines. Zero. The reason: real engines fail around a health value of about 0.26 in the raw sensor data, but the filter's own internal posterior sits higher than that at the same moment in time, around 0.34, because of how particles are initialised and how measurement noise behaves. Comparing against the wrong number added, on average, about a hundred spurious cycles to every prediction. The fix was to calibrate the failure threshold inside the filter's own posterior space, not the raw observation space, and to treat that threshold itself as uncertain, drawn separately for each particle. That one change took the credible interval from covering nothing to covering seventy-five to ninety-nine percent of engines, depending on the dataset.

## Slide 8
THE MODEL — PART 4
One Rate Doesn't Fit Every Engine
The degradation rate was first fit once, pooled across all 100 training engines — this understates the fleet's true average rate by ~26%, because it averages fast- and slow-failing engines together.
Fix 1 — PMMH
Estimate the growth rate and noise scale per engine as a Bayesian posterior (Particle Marginal Metropolis–Hastings), then aggregate into one fleet-wide pair.
Converged on 31/100 (FD001), 8/100 (FD003) engines — fallback used elsewhere.
Fix 2 — Similarity Library (adopted)
Keep one fitted rate per training engine. At test time, match the current engine to its closest analogues (MMD kernel) and borrow their rate.
Best point accuracy AND best-calibrated intervals on both datasets.
8
Notes: The second big source of error was the degradation rate itself. It was originally fit once, pooling all one hundred training engines together, and that pooled rate understates the fleet's true average rate by about twenty-six percent, because it averages fast-dying and slow-dying engines into one number. Two fixes address this. First, PMMH: a Bayesian method that estimates the rate and the noise scale per engine, then aggregates those into one fleet-wide pair -- it converged properly on thirty-one of the hundred FD001 engines and eight of a hundred on FD003, with a regression fallback elsewhere. Second, and this is the one I adopted as the final method: a similarity-based reference library. Instead of one rate for everyone, I keep a library of one rate per training engine, and at test time I match the engine currently being filtered to its closest analogues and borrow their rate. This is the method that ends up best on every accuracy and calibration metric.

## Slide 9
EXPERIMENTS
NASA C-MAPSS Turbofan Benchmark
 | FD001 | FD003
Operating conditions | 1 | 1
Fault mode(s) | HPC degradation | HPC + Fan degradation
Train / test engines | 100 / 100 | 100 / 100
Train cycle length (min/med/max) | 128 / 199 / 362 | 145 / 220 / 525
Test true RUL (min/med/max) | 7 / 86 / 145 | 6 / 77 / 145
FD003 is a robustness check: same pipeline, fitted only on FD001, tested unchanged on a harder, two-fault-mode dataset.
RMSE / MAPE
Point-accuracy — how close is the predicted RUL?
PHM08 score
Asymmetric penalty — late (over-)prediction costs more than early.
90% CI Coverage
Calibration — does the interval actually contain the truth? A point estimate cannot even report this.
9
Notes: The evaluation uses NASA's C-MAPSS turbofan benchmark. FD001 has a single fault mode and is the primary dataset; FD003 shares the same single operating condition but adds a second, independent fault mode, fan degradation on top of compressor degradation, and is used purely as a robustness check -- the pipeline is fit only on FD001 and reused unchanged on FD003. Both are evaluated on the full one-hundred-engine test fleet. Three kinds of metric are reported: RMSE and MAPE for point accuracy; the PHM08 competition score, which penalizes a late, over-confident prediction harder than an early, conservative one; and, most central to this thesis, ninety percent credible interval coverage -- whether the reported interval actually contains the truth. That last one is the metric a plain point-estimate model cannot report at all, because it has no interval to check.

## Slide 10
RESULTS
The Filter Tracks Health Well — Even on the Hardest Engines
0.08–0.09
Health-Index RMSE
(0–1 scale), fleet-wide
0.79 ± 0.02
Mean ESS / N — particle
cloud stays diverse
Figure 4.8 (thesis) — one-shot library, FD001: best (engine 76, left) vs. worst-tracked (engine 1, right) test engine. Even the worst case tracks health closely; its error shows up only in the RUL projection below.
10
Notes: This is Figure 4.8 directly from the thesis, so it is exactly what is in the version already sent to the committee. On the left is the best-tracked FD001 engine, on the right the worst-tracked -- engine 1, which is only observed for thirty-one cycles. Look at the top row first: even on the worst engine, the blue posterior median tracks the grey observed Health Index closely. Health tracking is not the problem. The problem only appears in the bottom row, the RUL projection: the orange predicted median and its interval sit well above the true countdown, the dashed line, because thirty-one cycles is simply not enough evidence for any method to lock onto that engine's true rate. Across the whole fleet, Health-Index RMSE is about eight to nine hundredths on a zero-to-one scale, and the effective sample size stays at seventy-nine percent of N on average -- so the filtering machinery itself is healthy across the board, not just on this one example.

## Slide 11
RESULTS
Accuracy and Calibration Improve Together
Method | FD001 RMSE | FD001 Coverage | FD003 RMSE | FD003 Coverage
Fixed parameters | 98.3 | 0.49 | 160.4 | 1.00
PMMH | 52.9 | 0.68 | 104.6 | 1.00
Library, one-shot (final) | 44.3 | 0.75 | 100.1 | 0.99
RMSE falls (cycles): 98.3 → 52.9 → 44.3 (FD001) Coverage rises: 0.49 → 0.68 → 0.75 (FD001, nominal target 0.90)
Every fix improves both accuracy and calibration at once — none trades one for the other.
Chart: 90% CI Coverage
| Fixed | PMMH | Library
FD001 coverage | 0.49 | 0.68 | 0.75
FD003 coverage | 1 | 1 | 0.99
nominal 0.90
11
Notes: This table is the heart of the results chapter. Reading FD001 left to right: RMSE drops from 98.3 cycles under fixed hand-set parameters, to 52.9 under PMMH, to 44.3 under the final library method. At the same time -- and this is the important point -- coverage of the ninety percent interval rises from 0.49, to 0.68, to 0.75. Every single fix improves both dimensions together; none of them trades accuracy for calibration or the other way round. FD003 tells a related but different story: RMSE also falls, from 160 to 100 cycles, but coverage is already at 1.00 and stays there -- meaning the interval on FD003 is wide enough to always contain the truth, so it is over-conservative rather than overconfident. I'll come back to why FD001 and FD003 fail in opposite directions in a moment.

## Slide 12
RESULTS
vs. Baseline: the Honest Trade-off
Chart: Point accuracy (lower is better)
| FD001 Baseline | FD001 Filter | FD003 Baseline | FD003 Filter
RMSE (cycles) | 32 | 44.3 | 58.2 | 100.1
The linear-regression baseline is the sharper point predictor on both datasets. But it reports no interval at all. Asking whether its 90% interval covers the truth isn't a poor result — it isn't even a question that can be posed. The filter concedes point accuracy and, in exchange, delivers a checkable, calibrated interval — 0.75 / 0.99 coverage — which is exactly the quantity a maintenance decision needs.
12
Notes: It would be dishonest to stop at the last slide without the direct comparison. A plain linear regression, given the exact same ten sensors, is actually the sharper point predictor: 32 cycles RMSE versus 44 for the filter on FD001, 58 versus 100 on FD003. So the argument for the particle filter does not rest on point accuracy, and it doesn't need to. What the baseline categorically cannot do is report a credible interval -- there is no distribution to check for coverage, the question doesn't even apply to it. The filter concedes some point accuracy and, in exchange, delivers a calibrated interval that covers seventy-five to ninety-nine percent of engines. For a maintenance decision, where acting too late risks an in-service failure, that calibrated uncertainty is the quantity that actually matters, not the sharpest possible point guess.

## Slide 13
HONEST ASSESSMENT
What's Left Imperfect
FD001: mildly overconfident
Coverage 0.75 vs nominal 0.90 — a single matched rate still can't capture every fast-degrading engine.
FD003: over-conservative
Coverage 0.99 — longer horizons + noisier library matches under two fault modes widen the interval.
PMMH convergence is partial
Chains converged on 31/100 (FD001) and 8/100 (FD003) engines; regression fallback used otherwise.
Scope: one operating condition
FD001/FD003 only — no operating-condition-aware normalisation yet for FD002/FD004.
13
Notes: In the interest of an honest defense, four things are not yet perfect. On FD001 the interval is mildly overconfident, 0.75 against a nominal 0.90, because a single matched rate per engine still cannot capture every fast-degrading engine exactly. On FD003 it's the opposite: 0.99, over-conservative, because run-to-failure horizons are longer and the similarity matching itself gets noisier once two fault modes are present. Third, PMMH's convergence was partial -- it properly converged on only thirty-one of a hundred FD001 engines and eight of a hundred FD003 engines, with a simpler regression fit used as a fallback for the rest; this is reported openly, not hidden. Fourth, the whole pipeline currently only handles a single operating condition -- extending it to FD002 and FD004, which vary operating conditions, would need an operating-condition-aware normalisation step that does not exist yet.

## Slide 14
WRAPPING UP
Conclusions & Future Work
Conclusions
• Architecture works: health tracked reliably, fleet-wide. • Point accuracy: final-cycle RMSE roughly halved (98.3 → 44.3 on FD001) by fitting the degradation rate from data. • Calibration: achieved in practice, not just in principle — coverage 0.000 → 0.75 / 0.99, checkable on a stated test fleet. • Contribution: a particle-filter digital twin with calibrated RUL, applied to turbofans — a gap the literature (battery-PF, DL-on-C-MAPSS) leaves open.
Future Work
Improve PMMH convergence; move to per-engine process noise
Jointly estimate growth rate and noise via PMMH + library
Life-fraction-normalised pooling (t / T_max) as an alternative fix
Formal Kernel Two-Sample Test for library matching (Cai et al. 2020)
Extend to FD002 / FD004 (multiple operating conditions)
Systematic particle-count sweep (N ∈ {500, 1000, 2000})
14
Notes: To conclude. The architecture works: the particle filter tracks engine health reliably across the whole fleet. Point accuracy improved substantially once the degradation rate was estimated from data instead of hand-set or pooled -- final-cycle RMSE on FD001 roughly halved. And calibration -- the dimension I frame as the actual reason to choose a probabilistic digital twin in the first place -- is achieved in practice, not merely available in principle: coverage moved from zero to seventy-five and ninety-nine percent, checkable on a stated hundred-engine test fleet, something a point-estimate deep-learning model cannot even offer. The contribution is combining a continuous-state particle filter with calibrated RUL and applying it to turbofan engines specifically, which the existing literature -- particle filters mostly on batteries, deep learning mostly reporting only point accuracy on C-MAPSS -- leaves as an open gap. For future work: better PMMH convergence and per-engine noise estimates are the most direct route to tightening the remaining calibration gap; beyond that, jointly estimating rate and noise, a life-fraction-normalised alternative to pooling, closing the similarity-matching simplifications, extending to more operating conditions, and a proper particle-count sensitivity sweep.

## Slide 15
Thank You
Questions welcome.
Sajjad Ayashm · s.ayashm@gmail.com
Notes: Thank you for your attention. I'm happy to take any questions.